## Slide 1
Learning to Push:
Imitation Learning and RL on PushT
Department of Mechanical Engineering
2026.10.07 (Wed)
Joo Yong Sim
Hands-on tutorial: pusht_imitation.py · pusht_rl.py · pusht_rl_realtime.py · pusht_rl_eval.py

## Slide 2
The PushT simulator from the dynamics lecture becomes a training ground
Physics
impulse · friction · walls
Demonstrations
human or scripted expert
Imitation
MLP-BC · Diffusion Policy
RL fine-tuning
PPO, started from BC
Three questions answered with experiments in this lecture
Q1 — Data : how many demonstrations do we need to collect?
Q2 — Model : which network should learn from them — a regressor or a generative model?
Q3 — Beyond imitation : can reinforcement learning do better, from scratch or starting from the imitation policy?
Pipeline : demonstrations → dataset → policy → closed-loop success rate on unseen tasks
Lecture Goals: From Physics to Policy
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
2

## Slide 3
One seed fixes the initial T pose, the goal pose and the pusher position
What
Distribution
T start pose
Goal pose
same; redrawn if too easy ( m and )
Pusher
uniform in the arena, from the T
Success
Seeds : demos use 100000+ (expert) and 200000+ (human); evaluation uses 0, 1, 2, … — tasks never seen in training.
Blue: T start · green dashed: goal · orange: pusher (seeds 0–7)
The PushT Task: Random Start, Random Goal
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
3

## Slide 4
The policy moves the pusher's target at 10 Hz; the physics runs 20 substeps in between
State (8 numbers — what a human sees)
Action
A PD controller pulls the pusher toward the target; contact with the T is the impulse model of the dynamics lecture.
One episode, saved to .npz
Array
Shape
Meaning
states
(N, 8)
actions
(N, 2)
= target
episode_ends
(E,)
where each episode ends
seeds
(E,)
re-creates the start
Only successful episodes are saved : imitating a failure teaches failure (filtered behavior cloning). Same format as the Diffusion Policy / LeRobot PushT data.
Control Loop and Demonstration Data
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
4

## Slide 5
python pusht_imitation.py collect — the keyboard simulator with a recorder added
Recorder window: arrows / WASD or mouse drag move the target; reaching the goal auto-saves
Three rules for clean data
Fixed 10 Hz : the screen draws at 20 fps, but is recorded every 0.1 s — one human step = one env.step().
Idle start trimmed : time spent thinking before the first move is not recorded, so the policy never learns to stand still.
Physics fixed : friction / restitution switches are off — same state, same consequence.
Keys : N new task · R restart · Backspace delete last · Space pause
Cost : one human demo takes 15–30 s, so 200 demos take 1.5–2 hours → we also need an automatic demonstrator.
Collecting Human Demonstrations
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
5

## Slide 6
A "virtual human" that chooses where to push with the lecture's impulse equations
(1) Where to push — unit impulse at candidate
Candidates : 8 edges × 3 points; = desired , = its effect.
(2) Approach : go to a standoff point; orbit around the T if the straight path is blocked.
(3) Push : along , slowing in proportion to the remaining error (the T slides after release).
Expert rollouts (orange: pusher path, colour: time) — success ≈ 88–91 % on random tasks
Scripted Expert: Impulse–Momentum as a Policy
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
6

## Slide 7
Published PushT and manipulation work uses 50–200 demonstrations per task
Source
Task
Demonstrations
Diffusion Policy (Chi et al., 2023)
PushT, fixed goal, random start
200 human (≈ 25k steps)
LeRobot pusht dataset
same task
206 episodes, 25,650 frames
ACT / ALOHA (Zhao et al., 2023)
real bimanual robot
50 per task
Suggested plan for human demonstrations (15–30 s each)
Stage
Demos
Time
Purpose
Pipeline check
10–20
10 min
save / load / train runs, loss goes down
First results
50–100
30–60 min
successes start; study the failures
Usable policy
≥ 200
1.5–2 h
Diffusion Policy paper scale
More important than the count : spread-out initial conditions, a consistent strategy, and discarded failures. Our goal is random too — harder than the original PushT.
How Many Demonstrations? Reference Points
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
7

## Slide 8
Ride along with the goal — the same idea as relative motion in rigid-body kinematics
Action representation (goal frame)
MLP-BC
Diffusion
absolute target position
26 %
20 %
offset from the current pusher
36 %
46 %
One training sample: goal at the origin, 0°
Without the goal frame : 0 % success for both models — a good representation saves data.
Goal Frame: Relative Motion Removes the Random Goal
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
8

## Slide 9
See two frames, plan eight actions, execute four, then re-plan
Observe
,
Predict
, (0.8 s)
Execute
first actions
Re-plan
receding horizon
Two frames : the difference gives velocity — is the T still sliding?
Chunks : one-step predictions change every 0.1 s and jitter; a chunk commits to a motion for a moment.
Normalize : , statistics from the training set only.
Split by episode : neighbouring steps are nearly identical — a step-wise split leaks data into validation.
Trade-off : 4 steps run open-loop, so an unexpected slide is corrected only at the next re-plan.
Observation History and Action Chunks
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
9

## Slide 10
MSE learns the average action — the average of two good actions can be bad
Toy problem: demonstrations avoid an obstacle up or down (50/50). MLP-BC learns — straight into it; Diffusion samples both modes.
In PushT : "go around the left or the right side of the T?" — MLP-BC hesitates in between; human demos are even more multimodal.
Which Model? The Multimodality Problem
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
10

## Slide 11
Learn a distribution instead of a single average action
Model
Output
Multimodal
Notes
MLP-BC (MSE)
one point
no (mean)
fastest, simplest — baseline
MLP-BC + action chunk
points
no
temporally consistent
GMM / MDN
Gaussians
partly
number of modes fixed in advance
VQ-BeT
discrete code + offset
yes
Transformer
ACT (CVAE + Transformer)
chunk
yes
real robot, 50 demos
Diffusion Policy
chunk, sampled
yes
standard PushT baseline, stable training
Our choice : MLP-BC as the baseline, Diffusion Policy as the main model — same MLP trunk (3 layers, width 512, Mish).
So the only difference is : learning the mean vs. learning the distribution.
Policy Model Candidates
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
11

## Slide 12
Learn to remove noise from action chunks; at run time, denoise noise into actions
1. Forward process: mix noise into a clean chunk
2. Training: predict the noise
3. Sampling: start from , step
Why it is multimodal : each run starts from different noise → a different sample → different modes of the demonstrations. Cosine schedule , .
Diffusion Policy (DDPM) in Three Steps
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
12

## Slide 13
Diffusion needs more capacity or more steps than MLP-BC before it pays off
Setting (180 expert demos, unseen tasks)
MLP-BC
Diffusion
width 256, lr , no EMA, 30k steps
32 %
8 %
width 256, lr + EMA, 30k steps
36–46 %
18–42 %
width 256, lr + EMA, 80k steps
—
64 %
width 512, lr + EMA, 30k steps (default)
38–59 %
54–63 %
width 512, lr + EMA, 50k steps
—
69 %
Batch 256, AdamW, cosine lr decay; about 1 min per model on GPU, 4 min on CPU.
Caution : re-running the same setting moves success by ±10 %; validation loss does not predict success (0.116 → 0.132 while 62 % → 69 %).
Training Settings Found by Experiment
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
13

## Slide 14
Diffusion reaches most of its performance at about 100 demonstrations
Experiment
400 expert demos → train on the first → width 512, 30k steps → 100 unseen tasks, closed loop.
Reading
Diffusion is ahead at every , most clearly with little data.
MLP-BC needs about 3× more demos for the same success.
Human demos : aim for at least 100, ideally 200.
Reproduce : tools/imitation_experiments/full/run_scale512.sh (10 jobs, about 15 min)
How Many Demonstrations? Measured
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
14

## Slide 15
Both learned policies stay below the expert that taught them
MLP-BC rollouts on unseen seeds
Diffusion Policy rollouts on the same seeds
MLP-BC : stalls or jitters beside the T — it averages between strategies.
Diffusion : commits to one strategy; fails at the final 0.15 m / 10° alignment or after one big mistake.
Both : covariate shift — their own errors lead to states never seen in the demos.
Default run (180 demos) : expert 88 % · MLP-BC 38–59 % · Diffusion 54–63 %. Remedy: DAgger — record human corrections.
Closed-Loop Rollouts and Failure Modes
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
15

## Slide 16
RL needs no demonstrations — only a reward and a great deal of trial and error
Experiment
Starting point
Result (50 unseen tasks, no exploration noise)
A. RL from scratch
random network
16.4M steps (2.5 h): 0 % success
B. BC → RL
MLP-BC policy
42 % → 74 % (3M) → 80 % (6M, 80 min)
Scripted expert
hand-written rules
88 %
Why A fails : success needs a long sequence — choose a contact, go around, push, align. Random motion almost never completes it, so the success bonus is never observed (the exploration problem).
Why B works : imitation already succeeds about half the time; RL only has to polish behaviour that works.
From Imitation to Reinforcement Learning
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
16

## Slide 17
Turn "how far is the task from done" into one number, and reward every step of progress
Remaining cost (1 rad ≈ 0.3 m)
Reward per step
Potential-based shaping : the progress term sums to — a signal every step, without changing the optimal policy.
Episode end : success is terminal; at 300 steps it is truncated and bootstrapped with .
Side effect : the time penalty makes RL finish faster than the expert, which has no such pressure.
Reward Design
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
17

## Slide 18
Collect 8,192 steps, estimate advantages, update for 10 epochs — repeat
Advantage (GAE),
Clipped objective,
Gaussian policy : sample while training, use the mean for evaluation.
A. scratch
B. BC → RL
Actor
2 × 256 tanh
the MLP-BC net
Initial
0.6
0.03 m
Actor lr
Critic
new
new, 10 warm-up updates
For B : clipping, a small learning rate and small noise protect the working BC policy from being destroyed early on.
PPO: Small, Clipped Policy Updates
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
18

## Slide 19
Pure-Python physics is slow, so 64 environments run at once on 16 CPU processes
Main process
policy for 64 observations at once
16 workers × 4 envs
physics, auto-reset on done
Benchmark (idle CPU, 20 cores)
Steps per PPO iteration
64 × 128 = 8,192
Rollout (physics 3.09 s)
3.79 s
PPO update
1.91 s (33 %)
Env steps / s
2,159 rollout · 1,437 total
Training wall-clock (from logs)
Run
Steps
Time
RL from scratch
16.4M
147 min
BC+PPO
0 → 6M
80 min
BC+PPO resumed
6 → 12M
70 min
Backend : CPU multiprocessing (fork + Pipe); the network also runs on the CPU. One environment alone would be ≈ 64× slower.
Parallel Simulation
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
19

## Slide 20
Starting from imitation turns an unsolvable exploration problem into fine-tuning
Training success with exploration noise (tutorial/checkpoints/rl/*/train_log*.txt)
From scratch : return improved −14 → −2.4, the T moves toward the goal, but 0 % success; exploration noise collapsed 0.6 → 0.03.
BC → RL : 0.44 → 0.88 in 6M steps, then a plateau at 0.87–0.90.
Lesson : demonstrations solve exploration; RL then optimizes what imitation cannot — the reward itself.
RL from Scratch vs BC → RL
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
20

## Slide 21
Same 100 unseen tasks, same start, 300 steps, deterministic actions for every policy
pusht_rl_eval.py → tutorial/eval_results/paired_*.csv / .json
Scripted vs BC+PPO
6M
12M
both succeed
74
70
only scripted
13
17
only BC+PPO
8
7
both fail
5
6
McNemar
0.38
0.064
median steps*
136 → 107
139 → 104
* on seeds both solved: scripted → BC+PPO
Result : success is statistically tied with the expert, and BC+PPO is about 3–4 s faster on the same tasks.
Paired Evaluation on Seeds 0–99
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
21

## Slide 22
More training made the policy faster, not more successful
Measured
Within noise : at 82 %, one standard error is about ±4 points with 100 tasks.
6M → 12M : success 82 % → 77 %, mean time 12.0 s → 11.1 s.
Plateau : training success stayed at 0.87–0.90 with noise .
Best checkpoint : 6M, not the newest 12M.
Likely structural limits (not yet tested)
Less information : 12 inputs vs. the expert's full state and memory.
Conservative updates : lr , clipping, small .
Reward ≠ success test : angle weighted 0.3; success needs 0.15 m and 10°.
One step at a time : BC drops 54 % → 34 % without chunks.
Not a ceiling : RL optimizes the reward, not imitation — align the reward with the success test to push further.
Why BC+PPO Stops Near the Expert
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
22

## Slide 23
python pusht_rl_realtime.py — every panel replays the same random task live
Seed 30: script 8.7 s · BC→RL 6.4 / 6.2 s · BC and RL-from-scratch time out
Run
cd tutorial
python pusht_rl_realtime.py
python pusht_rl_realtime.py script
python pusht_rl.py eval
python pusht_rl_eval.py
Keys
Space pause · N next task · + / − speed · Q quit
Real-Time Demo: Five Policies, One Task
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
23

## Slide 24
•
Imitation learning = supervised learning on from successful demonstrations
→
Goal frame (relative motion) and action offsets matter as much as the model
•
Data: about 100 demos for Diffusion Policy; collect 100–200 human demos
•
Model: MSE learns ; Diffusion learns the distribution and handles multimodality
→
Measured: Diffusion 20–68 % vs MLP-BC 9–59 % (25–360 demos)
•
RL from scratch: 0 % after 16M steps — the exploration problem
→
BC → PPO: 54 % → 82 % on seeds 0–99, tied with the expert (87 %) and 3–4 s faster
Physics gives the data, imitation gives the start, RL gives the polish
Summary
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
24

## Slide 25
•
Human data : collect 50, then 100 demos — does the Diffusion vs MLP-BC gap grow?
•
No goal frame : train in world coordinates — how much success is lost?
•
Chunks : vary the prediction / execution horizons (1, 4, 8, 16)
•
History : one observation frame — which mistakes appear without velocity?
•
DAgger : record your corrections in the viewer and retrain
•
Robustness : evaluate with friction 0.2 instead of 0.4 — think domain randomization
•
RL : put the 0.15 m / 10° test into the reward — does BC+PPO pass the expert?
Exercises with the tutorial code
Try It Yourself
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
25