## Slide 1
Learning to Push:
Imitation Learning and RL on PushT
Department of Mechanical Engineering
2026.10.07 (Wed)
Joo Yong Sim
Extended edition: contact physics derived and compared line by line with the tutorial code

## Slide 2
The PushT simulator from the dynamics lecture becomes a training ground
Physics
impulse · friction · walls
Demonstrations
human or scripted expert
Imitation
MLP-BC · Diffusion Policy
RL fine-tuning
PPO, started from BC
Three questions answered with experiments in this lecture
Q1 — Data : how many demonstrations do we need to collect?
Q2 — Model : which network should learn from them — a regressor or a generative model?
Q3 — Beyond imitation : can reinforcement learning do better, from scratch or starting from the imitation policy?
Pipeline : demonstrations → dataset → policy → closed-loop success rate on unseen tasks
Lecture Goals: From Physics to Policy
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
2

## Slide 3
One seed fixes the initial T pose, the goal pose and the pusher position
What
Distribution
T start pose
Goal pose
same; redrawn if too easy ( m and )
Pusher
uniform in the arena, from the T
Success
Seeds : demos use 100000+ (expert) and 200000+ (human); evaluation uses 0, 1, 2, … — tasks never seen in training.
Blue: T start · green dashed: goal · orange: pusher (seeds 0–7)
The PushT Task: Random Start, Random Goal
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
3

## Slide 4
The policy moves the pusher's target at 10 Hz; the physics runs 20 substeps in between
State (8 numbers — what a human sees)
Action
A PD controller pulls the pusher toward the target; contact with the T is the impulse model of the dynamics lecture.
One episode, saved to .npz
Array
Shape
Meaning
states
(N, 8)
actions
(N, 2)
= target
episode_ends
(E,)
where each episode ends
seeds
(E,)
re-creates the start
Only successful episodes are saved : imitating a failure teaches failure (filtered behavior cloning). Same format as the Diffusion Policy / LeRobot PushT data.
Control Loop and Demonstration Data
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
4

## Slide 5
One env.step() = 0.1 s = 20 substeps of 5 ms, each with a 3-pass contact solver
Target
PD pusher
Contact
point, , depth
Impulse
T motion
Time steps
Average contact force
pusht_imitation.py : PushTEnv.step · pusht_keyboard_sim.py : advance
def step(self, action):
self.sim.target = np.clip(action, [x_min, y_min], [x_max, y_max])
self.sim.advance(self.control_dt) # 0.1 s
self.t += 1
def advance(self, frame_dt):
n = max(1, int(round(frame_dt / self.physics_dt)))
self._j_sum[:] = 0.0
for _ in range(n):
self.substep(self.physics_dt) # 5 ms
F = self._j_sum / (n * self.physics_dt) # impulse / time
Physics Inside One Control Step
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
5

## Slide 6
The pusher is a controlled kinematic body; the T coasts and slows down by floor friction
1. PD control of the pusher
: damping ratio — fast, no overshoot. Speed limited to m/s.
2. Floor friction as exponential decay
3. Semi-implicit Euler
pusht_keyboard_sim.py : KeyboardPushT.substep
# 1. pusher PD control toward the target
acc = self.kp * (self.target - P.pos) - self.kd * P.vel
P.vel += acc * dt
speed = np.linalg.norm(P.vel)
if speed > self.max_speed:
P.vel *= self.max_speed / speed
P.pos += P.vel * dt # new velocity first
# 2. damping 3. integrate the T
T.vel *= math.exp(-self.linear_damping * dt)
T.omega *= math.exp(-self.angular_damping * dt)
T.pos += T.vel * dt
T.angle += T.omega * dt
Consequence : released at speed , the T slides another — the expert slows down near the goal for this reason.
Substep: PD Pusher, Damping, Integration
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
6

## Slide 7
Composite body: two rectangles, each shifted to the T's centre of mass
Centre of mass (mass ∝ area)
Rectangle + parallel-axis theorem
Value ()
Result
top bar
stem
COM below the top edge
0.627
0.434
pusht_keyboard_sim.py : make_T_geometry
top_area = W * top_t
stem_h = H - top_t
stem_area = stem_w * stem_h
total_area = top_area + stem_area
y_top, y_stem = H / 2 - top_t / 2, -top_t / 2
y_com = (top_area * y_top + stem_area * y_stem) / total_area
m_top = mass * top_area / total_area
m_stem = mass * stem_area / total_area
# own centre + parallel-axis shift to the COM
I_top = m_top * (W**2 + top_t**2) / 12 \
+ m_top * (y_top - y_com) ** 2
I_stem = m_stem * (stem_w**2 + stem_h**2) / 12 \
+ m_stem * (y_stem - y_com) ** 2
vertices[:, 1] -= y_com # body origin = COM
T Geometry: Mass Moment of Inertia
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
7

## Slide 8
Work in the T's own frame: closest point on the 8 edges, then inside / outside
World → body frame
Closest point on edge
Penetration (pusher radius )
pusht_imitation.py : circle_vs_T_fast (all edges at once)
R = rotation_matrix(body_angle)
c = R.T @ (circle_pos - body_pos) # world -> T
A = vertices
AB = np.roll(vertices, -1, axis=0) - A
t = np.clip(((c - A) * AB).sum(1) / (AB * AB).sum(1), 0, 1)
Q = A + t[:, None] * AB # closest points
d2 = ((Q - c) ** 2).sum(1)
i = int(np.argmin(d2))
d = math.sqrt(d2[i])
inside = ... # ray casting
if not inside and d >= radius:
return None
direction = (Q[i] - c) / d
n_local, pen = (-direction, radius + d) if inside \
else (direction, radius - d)
n = R @ n_local
return body_pos + R @ Q[i], n, pen
Speed : the numpy version replaces an 8-iteration Python loop — identical results on 2000 random cases, checked in the tutorial.
Contact Detection: Circle vs T
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
8

## Slide 9
Relative velocity says whether the bodies approach; an impulse stops them
Velocity of the contact point
Normal impulse
pusht_keyboard_sim.py : resolve_impulse (part 1)
point, n, pen = contact
r = point - body.pos
v_rel = body.vel + omega_cross_r(body.omega, r) - other_vel
v_n = float(np.dot(v_rel, n))
if v_n < 0: # approaching
K_n = 1.0 / body.mass + cross2(r, n) ** 2 / body.inertia
j_n = -(1.0 + restitution) * v_n / K_n
J = j_n * n
body.vel += J / body.mass
body.omega += cross2(r, J) / body.inertia
def cross2(a, b): # 2D cross product, z only
return a[0] * b[1] - a[1] * b[0]
Kinematic pusher : , so only the T's terms remain in . PushT uses — after impact .
Contact Velocity and Normal Impulse
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
9

## Slide 10
The same push at a different height splits into translation and rotation differently
Derivation: normal velocity change at C
Stem's left face (), , :
Height
0 (COM)
1.000
1.000
1.000
0.000
−0.5
1.576
0.634
0.634
0.731
−1.0
3.305
0.303
0.303
0.697
Output of resolve_impulse() — pusht_mini_sim.py, section 8
At the COM : pure translation. Far from the COM : smaller impulse, mostly rotation.
This is PushT : choosing the contact point chooses the motion — exactly what the scripted expert and the learned policies must do.
Why Contact Height Matters
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
10

## Slide 11
Cancel the sliding velocity at the contact, but never beyond
Tangent direction
Impulse that stops sliding
Coulomb limit
pusht_keyboard_sim.py : resolve_impulse (part 2)
# friction, using the velocity after the normal impulse
t = np.array([-n[1], n[0]])
v_rel = body.vel + omega_cross_r(body.omega, r) - other_vel
v_t = float(np.dot(v_rel, t))
K_t = 1.0 / body.mass + cross2(r, t) ** 2 / body.inertia
j_t = float(np.clip(-v_t / K_t,
-friction * j_n, friction * j_n))
Jt = j_t * t
body.vel += Jt / body.mass
body.omega += cross2(r, Jt) / body.inertia
Effect : with friction the pusher can drag the T sideways and rotate it; with it slips along the surface (try F in the keyboard demo).
Coulomb Friction Impulse
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
11

## Slide 12
A wall is a kinematic body with zero velocity — the same impulse function handles it
Wall = pusher with
Left wall:
Penetration correction
Discrete time jumps leave overlaps that impulses alone cannot remove.
pusht_keyboard_sim.py : wall_contacts · substep (step 4)
world = body.pos + body.vertices @ rotation_matrix(body.angle).T
for p in world:
for depth, n in ((x_min - p[0], (1.0, 0.0)), ...):
if depth > 0:
contacts.append((p.copy(), np.array(n), depth))
# 4. contact solver: pusher-T and wall-T
for _ in range(3):
c = circle_vs_T(P.pos, P.radius, T.pos, T.angle, T.vertices)
if c is not None:
jn, jt = resolve_impulse(T, P.vel, c, e, mu)
for w in wall_contacts(T):
resolve_impulse(T, np.zeros(2), w, e, mu)
# end of resolve_impulse
body.pos += 0.8 * max(pen - 1e-4, 0.0) * n
Walls and Penetration Correction
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
12

## Slide 13
Every line of the simulator is an equation from the dynamics lecture
Lecture idea
Equation
Code
PD control
substep, step 1
Parallel-axis theorem
make_T_geometry
Relative velocity
omega_cross_r
Restitution
j_n = -(1+e) v_n / K_n
Linear impulse–momentum
body.vel += J / m
Angular impulse–momentum
body.omega += cross2(r, J) / I
Coulomb friction
np.clip(-v_t / K_t, ...)
Impulse = force × time
advance
Files : derivations in pusht_mini_sim.py · real-time version in pusht_keyboard_sim.py · random tasks in pusht_imitation.py
Physics Summary: Equation ↔ Code
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
13

## Slide 14
python pusht_imitation.py collect — the keyboard simulator with a recorder added
Recorder window: arrows / WASD or mouse drag move the target; reaching the goal auto-saves
Three rules for clean data
Fixed 10 Hz : the screen draws at 20 fps, but is recorded every 0.1 s — one human step = one env.step().
Idle start trimmed : time spent thinking before the first move is not recorded, so the policy never learns to stand still.
Physics fixed : friction / restitution switches are off — same state, same consequence.
Keys : N new task · R restart · Backspace delete last · Space pause
Cost : one human demo takes 15–30 s, so 200 demos take 1.5–2 hours → we also need an automatic demonstrator.
Collecting Human Demonstrations
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
14

## Slide 15
A "virtual human" that chooses where to push with the lecture's impulse equations
(1) Where to push — unit impulse at candidate
Candidates : 8 edges × 3 points; = desired , = its effect.
(2) Approach : go to a standoff point; orbit around the T if the straight path is blocked.
(3) Push : along , slowing in proportion to the remaining error (the T slides after release).
Expert rollouts (orange: pusher path, colour: time) — success ≈ 88–91 % on random tasks
Scripted Expert: Impulse–Momentum as a Policy
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
15

## Slide 16
Score each candidate push by how well its impulse response points toward the goal
Desired change ()
Response to a unit impulse at
Cosine score
Penalty for pushing into a touching wall; +0.1 for keeping the same contact.
pusht_imitation.py : ScriptedExpert.act
e = sim.goal_pos - T.pos
d = np.array([e[0], e[1],
self.L * wrap_angle(sim.goal_angle - T.angle)])
for k, (c_local, out_local) in enumerate(self.cands):
cw, out = T.pos + R @ c_local, R @ out_local
n_in, r = -out, cw - T.pos
c = np.array([n_in[0] / T.mass, n_in[1] / T.mass,
self.L * cross2(r, n_in) / T.inertia])
score = c @ d / (np.linalg.norm(c) * d_norm + 1e-9)
for n_wall in walls:
if n_in @ np.array(n_wall) < -0.3:
score -= 0.6 # into that wall
if k == self.cur:
score += 0.1 # hysteresis
# push: slower when close to the goal
step = float(np.clip(0.3 * d_norm, 0.04, 0.12))
return P.pos - out * (step + 0.04)
Scripted Expert: Equation ↔ Code
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
16

## Slide 17
Published PushT and manipulation work uses 50–200 demonstrations per task
Source
Task
Demonstrations
Diffusion Policy (Chi et al., 2023)
PushT, fixed goal, random start
200 human (≈ 25k steps)
LeRobot pusht dataset
same task
206 episodes, 25,650 frames
ACT / ALOHA (Zhao et al., 2023)
real bimanual robot
50 per task
Suggested plan for human demonstrations (15–30 s each)
Stage
Demos
Time
Purpose
Pipeline check
10–20
10 min
save / load / train runs, loss goes down
First results
50–100
30–60 min
successes start; study the failures
Usable policy
≥ 200
1.5–2 h
Diffusion Policy paper scale
More important than the count : spread-out initial conditions, a consistent strategy, and discarded failures. Our goal is random too — harder than the original PushT.
How Many Demonstrations? Reference Points
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
17

## Slide 18
Ride along with the goal — the same idea as relative motion in rigid-body kinematics
Action representation (goal frame)
MLP-BC
Diffusion
absolute target position
26 %
20 %
offset from the current pusher
36 %
46 %
One training sample: goal at the origin, 0°
Without the goal frame : 0 % success for both models — a good representation saves data.
Goal Frame: Relative Motion Removes the Random Goal
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
18

## Slide 19
A rotation and a translation — written out by hand so it works on any batch shape
State layout: → indices 0–7.
pusht_imitation.py : to_goal_frame · make_obs · action_to_model
def to_goal_frame(points, state, origin=None):
c, s = math.cos(state[7]), math.sin(state[7])
v = points - (state[5:7] if origin is None else origin)
return np.stack([ c * v[..., 0] + s * v[..., 1],
-s * v[..., 0] + c * v[..., 1]], -1)
def make_obs(state):
p = to_goal_frame(state[0:2], state)
T = to_goal_frame(state[2:4], state)
dth = state[4] - state[7]
return np.array([p[0], p[1], T[0], T[1],
math.cos(dth), math.sin(dth)])
def action_to_model(actions, state):
return to_goal_frame(actions, state, origin=state[0:2])
Goal Frame: Equation ↔ Code
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
19

## Slide 20
See two frames, plan eight actions, execute four, then re-plan
Observe
,
Predict
, (0.8 s)
Execute
first actions
Re-plan
receding horizon
Two frames : the difference gives velocity — is the T still sliding?
Chunks : one-step predictions change every 0.1 s and jitter; a chunk commits to a motion for a moment.
Normalize : , statistics from the training set only.
Split by episode : neighbouring steps are nearly identical — a step-wise split leaks data into validation.
Trade-off : 4 steps run open-loop, so an unexpected slide is corrected only at the next re-plan.
Observation History and Action Chunks
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
20

## Slide 21
MSE learns the average action — the average of two good actions can be bad
Toy problem: demonstrations avoid an obstacle up or down (50/50). MLP-BC learns — straight into it; Diffusion samples both modes.
In PushT : "go around the left or the right side of the T?" — MLP-BC hesitates in between; human demos are even more multimodal.
Which Model? The Multimodality Problem
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
21

## Slide 22
Learn a distribution instead of a single average action
Model
Output
Multimodal
Notes
MLP-BC (MSE)
one point
no (mean)
fastest, simplest — baseline
MLP-BC + action chunk
points
no
temporally consistent
GMM / MDN
Gaussians
partly
number of modes fixed in advance
VQ-BeT
discrete code + offset
yes
Transformer
ACT (CVAE + Transformer)
chunk
yes
real robot, 50 demos
Diffusion Policy
chunk, sampled
yes
standard PushT baseline, stable training
Our choice : MLP-BC as the baseline, Diffusion Policy as the main model — same MLP trunk (3 layers, width 512, Mish).
So the only difference is : learning the mean vs. learning the distribution.
Policy Model Candidates
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
22

## Slide 23
Learn to remove noise from action chunks; at run time, denoise noise into actions
1. Forward process: mix noise into a clean chunk
2. Training: predict the noise
3. Sampling: start from , step
Why it is multimodal : each run starts from different noise → a different sample → different modes of the demonstrations. Cosine schedule , .
Diffusion Policy (DDPM) in Three Steps
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
23

## Slide 24
Training is one line of noise mixing; sampling is a loop of K = 50 denoising steps
Training
Sampling
pusht_imitation.py : DiffusionPolicy.loss · predict
def loss(self, x, y):
a0 = self.ny(y)
k = torch.randint(0, self.K, (len(a0),))
eps = torch.randn_like(a0)
ab = self.abar[k][:, None]
a_k = ab.sqrt() * a0 + (1 - ab).sqrt() * eps
return ((self.eps_hat(a_k, k, self.nx(x)) - eps) ** 2).mean()
def predict(self, x):
a = torch.randn(len(xn), self.d_act) # a^K ~ N(0, I)
for k in reversed(range(self.K)):
ab = self.abar[k]
a0 = (a - (1 - ab).sqrt() * self.eps_hat(a, kk, xn)) / ab.sqrt()
mean = (ab_prev.sqrt() * self.betas[k] / (1 - ab)) * a0 \
+ (self.alphas[k].sqrt() * (1 - ab_prev) / (1 - ab)) * a
var = self.betas[k] * (1 - ab_prev) / (1 - ab)
a = mean + var.sqrt() * torch.randn_like(a)
Diffusion Policy: Equation ↔ Code
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
24

## Slide 25
Diffusion needs more capacity or more steps than MLP-BC before it pays off
Setting (180 expert demos, unseen tasks)
MLP-BC
Diffusion
width 256, lr , no EMA, 30k steps
32 %
8 %
width 256, lr + EMA, 30k steps
36–46 %
18–42 %
width 256, lr + EMA, 80k steps
—
64 %
width 512, lr + EMA, 30k steps (default)
38–59 %
54–63 %
width 512, lr + EMA, 50k steps
—
69 %
Batch 256, AdamW, cosine lr decay; about 1 min per model on GPU, 4 min on CPU.
Caution : re-running the same setting moves success by ±10 %; validation loss does not predict success (0.116 → 0.132 while 62 % → 69 %).
Training Settings Found by Experiment
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
25

## Slide 26
Diffusion reaches most of its performance at about 100 demonstrations
Experiment
400 expert demos → train on the first → width 512, 30k steps → 100 unseen tasks, closed loop.
Reading
Diffusion is ahead at every , most clearly with little data.
MLP-BC needs about 3× more demos for the same success.
Human demos : aim for at least 100, ideally 200.
Reproduce : tools/imitation_experiments/full/run_scale512.sh (10 jobs, about 15 min)
How Many Demonstrations? Measured
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
26

## Slide 27
Both learned policies stay below the expert that taught them
MLP-BC rollouts on unseen seeds
Diffusion Policy rollouts on the same seeds
MLP-BC : stalls or jitters beside the T — it averages between strategies.
Diffusion : commits to one strategy; fails at the final 0.15 m / 10° alignment or after one big mistake.
Both : covariate shift — their own errors lead to states never seen in the demos.
Default run (180 demos) : expert 88 % · MLP-BC 38–59 % · Diffusion 54–63 %. Remedy: DAgger — record human corrections.
Closed-Loop Rollouts and Failure Modes
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
27

## Slide 28
RL needs no demonstrations — only a reward and a great deal of trial and error
Experiment
Starting point
Result (50 unseen tasks, no exploration noise)
A. RL from scratch
random network
16.4M steps (2.5 h): 0 % success
B. BC → RL
MLP-BC policy
42 % → 74 % (3M) → 80 % (6M, 80 min)
Scripted expert
hand-written rules
88 %
Why A fails : success needs a long sequence — choose a contact, go around, push, align. Random motion almost never completes it, so the success bonus is never observed (the exploration problem).
Why B works : imitation already succeeds about half the time; RL only has to polish behaviour that works.
From Imitation to Reinforcement Learning
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
28

## Slide 29
Turn "how far is the task from done" into one number, and reward every step of progress
Remaining cost (1 rad ≈ 0.3 m)
Reward per step
Potential-based shaping : the progress term sums to — a signal every step, without changing the optimal policy.
Episode end : success is terminal; at 300 steps it is truncated and bootstrapped with .
Side effect : the time penalty makes RL finish faster than the expert, which has no such pressure.
Reward Design
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
29

## Slide 30
Two short functions — the RL training loop calls them once per environment step
: positive when the T moved closer to the goal pose.
wrap_angle keeps in , so counts as .
pusht_rl.py : task_cost · reward
def task_cost(sim):
return float(np.linalg.norm(sim.T.pos - sim.goal_pos)
+ 0.3 * abs(wrap_angle(sim.T.angle - sim.goal_angle)))
def reward(c_before, c_after, sim, success):
dist_pt = float(np.linalg.norm(sim.pusher.pos - sim.T.pos))
return (10.0 * (c_before - c_after)
- 0.02 * max(dist_pt - 1.0, 0.0)
- 0.01
+ (10.0 if success else 0.0))
Reward: Equation ↔ Code
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
30

## Slide 31
Collect 8,192 steps, estimate advantages, update for 10 epochs — repeat
Advantage (GAE),
Clipped objective,
Gaussian policy : sample while training, use the mean for evaluation.
A. scratch
B. BC → RL
Actor
2 × 256 tanh
the MLP-BC net
Initial
0.6
0.03 m
Actor lr
Critic
new
new, 10 warm-up updates
For B : clipping, a small learning rate and small noise protect the working BC policy from being destroyed early on.
PPO: Small, Clipped Policy Updates
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
31

## Slide 32
GAE runs backwards through the rollout; the clipped loss is one line
Advantage, backwards in time
Clipped surrogate
pusht_rl.py : train loop
for t in reversed(range(n_steps)): # GAE
nv = v_next if t == n_steps - 1 else V[t + 1]
delta = R[t] + gamma * nv * (1 - DONE[t]) - V[t]
g = delta + gamma * lam * (1 - DONE[t]) * g
adv[t] = g
RET = ADV + torch.cat(V) # critic target
for _ in range(10): # PPO epochs
...
lv = ((model.value(Ob[idx]) - RET[idx]) ** 2).mean()
if it >= critic_warmup:
ratio = (policy_dist(model, Ob[idx]).log_prob(Ab[idx])
.sum(-1) - LPb[idx]).exp()
la = -torch.min(ratio * ADV[idx],
ratio.clamp(0.8, 1.2) * ADV[idx]).mean()
PPO: Equation ↔ Code
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
32

## Slide 33
Pure-Python physics is slow, so 64 environments run at once on 16 CPU processes
Main process
policy for 64 observations at once
16 workers × 4 envs
physics, auto-reset on done
Benchmark (idle CPU, 20 cores)
Steps per PPO iteration
64 × 128 = 8,192
Rollout (physics 3.09 s)
3.79 s
PPO update
1.91 s (33 %)
Env steps / s
2,159 rollout · 1,437 total
Training wall-clock (from logs)
Run
Steps
Time
RL from scratch
16.4M
147 min
BC+PPO
0 → 6M
80 min
BC+PPO resumed
6 → 12M
70 min
Backend : CPU multiprocessing (fork + Pipe); the network also runs on the CPU. One environment alone would be ≈ 64× slower.
Parallel Simulation
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
33

## Slide 34
Starting from imitation turns an unsolvable exploration problem into fine-tuning
Training success with exploration noise (tutorial/checkpoints/rl/*/train_log*.txt)
From scratch : return improved −14 → −2.4, the T moves toward the goal, but 0 % success; exploration noise collapsed 0.6 → 0.03.
BC → RL : 0.44 → 0.88 in 6M steps, then a plateau at 0.87–0.90.
Lesson : demonstrations solve exploration; RL then optimizes what imitation cannot — the reward itself.
RL from Scratch vs BC → RL
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
34

## Slide 35
Same 100 unseen tasks, same start, 300 steps, deterministic actions for every policy
pusht_rl_eval.py → tutorial/eval_results/paired_*.csv / .json
Scripted vs BC+PPO
6M
12M
both succeed
74
70
only scripted
13
17
only BC+PPO
8
7
both fail
5
6
McNemar
0.38
0.064
median steps*
136 → 107
139 → 104
* on seeds both solved: scripted → BC+PPO
Result : success is statistically tied with the expert, and BC+PPO is about 3–4 s faster on the same tasks.
Paired Evaluation on Seeds 0–99
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
35

## Slide 36
More training made the policy faster, not more successful
Measured
Within noise : at 82 %, one standard error is about ±4 points with 100 tasks.
6M → 12M : success 82 % → 77 %, mean time 12.0 s → 11.1 s.
Plateau : training success stayed at 0.87–0.90 with noise .
Best checkpoint : 6M, not the newest 12M.
Likely structural limits (not yet tested)
Less information : 12 inputs vs. the expert's full state and memory.
Conservative updates : lr , clipping, small .
Reward ≠ success test : angle weighted 0.3; success needs 0.15 m and 10°.
One step at a time : BC drops 54 % → 34 % without chunks.
Not a ceiling : RL optimizes the reward, not imitation — align the reward with the success test to push further.
Why BC+PPO Stops Near the Expert
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
36

## Slide 37
python pusht_rl_realtime.py — every panel replays the same random task live
Seed 30: script 8.7 s · BC→RL 6.4 / 6.2 s · BC and RL-from-scratch time out
Run
cd tutorial
python pusht_rl_realtime.py
python pusht_rl_realtime.py script
python pusht_rl.py eval
python pusht_rl_eval.py
Keys
Space pause · N next task · + / − speed · Q quit
Real-Time Demo: Five Policies, One Task
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
37

## Slide 38
•
Imitation learning = supervised learning on from successful demonstrations
→
Goal frame (relative motion) and action offsets matter as much as the model
•
Data: about 100 demos for Diffusion Policy; collect 100–200 human demos
•
Model: MSE learns ; Diffusion learns the distribution and handles multimodality
→
Measured: Diffusion 20–68 % vs MLP-BC 9–59 % (25–360 demos)
•
RL from scratch: 0 % after 16M steps — the exploration problem
→
BC → PPO: 54 % → 82 % on seeds 0–99, tied with the expert (87 %) and 3–4 s faster
Physics gives the data, imitation gives the start, RL gives the polish
Summary
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
38

## Slide 39
•
Human data : collect 50, then 100 demos — does the Diffusion vs MLP-BC gap grow?
•
No goal frame : train in world coordinates — how much success is lost?
•
Chunks : vary the prediction / execution horizons (1, 4, 8, 16)
•
History : one observation frame — which mistakes appear without velocity?
•
DAgger : record your corrections in the viewer and retrain
•
Robustness : evaluate with friction 0.2 instead of 0.4 — think domain randomization
•
RL : put the 0.15 m / 10° test into the reward — does BC+PPO pass the expert?
Exercises with the tutorial code
Try It Yourself
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
39