## Slide 1
Learning to Push:
Imitation Learning and RL on PushT
Department of Mechanical Engineering
2026.10.07 (Wed)
Joo Yong Sim
Step-by-step edition: from basic physics, learning and RL to the full PushT pipeline

## Slide 2
Five parts — each one uses only what the parts before it built
Basic physics
Steps 1–7
PushT simulator
contact code
Learning from demos
Steps 8–11
Basic RL
Steps 12–18
Results
paired evaluation
Part
Key question
Tutorial file
Basic physics
How does a computer move a rigid body and resolve a collision?
pusht_mini_sim.py
PushT simulator
Which line of code is which equation?
pusht_keyboard_sim.py
Learning from demos
How does a network copy a demonstrator?
pusht_imitation.py
Basic RL
How does an agent improve from reward alone?
pusht_rl.py
Results
Which policy works best, and why?
pusht_rl_eval.py
Prerequisites : and impulse–momentum from the dynamics lecture, vectors and matrices, basic Python.
Roadmap: From Newton's Law to PPO
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
2

## Slide 3
The PushT simulator from the dynamics lecture becomes a training ground
Physics
impulse · friction · walls
Demonstrations
human or scripted expert
Imitation
MLP-BC · Diffusion Policy
RL fine-tuning
PPO, started from BC
Three questions answered with experiments in this lecture
Q1 — Data : how many demonstrations do we need to collect?
Q2 — Model : which network should learn from them — a regressor or a generative model?
Q3 — Beyond imitation : can reinforcement learning do better, from scratch or starting from the imitation policy?
Pipeline : demonstrations → dataset → policy → closed-loop success rate on unseen tasks
Lecture Goals: From Physics to Policy
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
3

## Slide 4
One seed fixes the initial T pose, the goal pose and the pusher position
What
Distribution
T start pose
Goal pose
same; redrawn if too easy ( m and )
Pusher
uniform in the arena, from the T
Success
Seeds : demos use 100000+ (expert) and 200000+ (human); evaluation uses 0, 1, 2, … — tasks never seen in training.
Blue: T start · green dashed: goal · orange: pusher (seeds 0–7)
The PushT Task: Random Start, Random Goal
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
4

## Slide 5
The policy moves the pusher's target at 10 Hz; the physics runs 20 substeps in between
State (8 numbers — what a human sees)
Action
A PD controller pulls the pusher toward the target; contact with the T is the impulse model of the dynamics lecture.
One episode, saved to .npz
Array
Shape
Meaning
states
(N, 8)
actions
(N, 2)
= target
episode_ends
(E,)
where each episode ends
seeds
(E,)
re-creates the start
Only successful episodes are saved : imitating a failure teaches failure (filtered behavior cloning). Same format as the Diffusion Policy / LeRobot PushT data.
Control Loop and Demonstration Data
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
5

## Slide 6
A computer cannot integrate continuously — it advances the state in small steps
Continuous
Discrete: semi-implicit Euler
Semi-implicit : the position uses the new velocity — stable for springs and PD controllers where explicit Euler gains energy.
Generic loop · pusht_keyboard_sim.py : substep
# a particle under a force, step by step
dt = 0.005
for k in range(n_steps):
a = force(x, v) / m # Newton: a = F / m
v = v + a * dt # velocity first
x = x + v * dt # then position
# the same two lines for the PushT pusher
P.vel += acc * dt
P.pos += P.vel * dt
Step size : PushT uses ms. Smaller is more accurate but slower — accuracy vs. speed matters again when RL needs millions of steps.
Step 1 · Newton's Law in Discrete Time
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
6

## Slide 7
The floor removes momentum — model it as a force proportional to velocity
Viscous floor friction
Exact discrete update — stable for any
m/s,
Value
95 % of speed lost
s
total slide
m
pusht_keyboard_sim.py : substep (step 2)
self.linear_damping = 3.0 # c_v [1/s]
self.angular_damping = 3.0 # c_w [1/s]
T.vel *= math.exp(-self.linear_damping * dt)
T.omega *= math.exp(-self.angular_damping * dt)
Two friction models : the floor uses this simple viscous law; the pusher–T contact uses Coulomb friction (later).
Step 2 · Friction Slows a Sliding Body
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
7

## Slide 8
Three numbers place the T, ; three more describe its motion,
Equations of motion (plane)
Where is a body point?
Rotation is integrated like translation
pusht_keyboard_sim.py · pusht_imitation.py
@dataclass
class TBody:
pos: np.ndarray # x_G, y_G
angle: float # theta
vel: np.ndarray # v_G
omega: float
mass: float
inertia: float # I_G
vertices: np.ndarray # p_local, COM at 0
def rotation_matrix(theta):
c, s = np.cos(theta), np.sin(theta)
return np.array([[c, -s], [s, c]])
def T_outline(pos, angle, vertices):
return pos + vertices @ rotation_matrix(angle).T
In PushT : apart from floor damping, every push reaches the T as an impulse — so and change by jumps (Steps 5–6).
Step 3 · A Rigid Body: Translation + Rotation
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
8

## Slide 9
Every point shares , plus a rotational part perpendicular to
In 2D,
Worked example
m/s, rad/s, m
That point is momentarily at rest — the instantaneous centre of the dynamics lecture.
pusht_keyboard_sim.py
def omega_cross_r(omega, r):
"""[0, 0, omega] x [rx, ry, 0]"""
return np.array([-omega * r[1], omega * r[0]])
def cross2(a, b):
"""2D cross product a x b -> scalar (z)"""
return float(a[0] * b[1] - a[1] * b[0])
# used for the contact point:
v_C = body.vel + omega_cross_r(body.omega, r)
Why it matters : a collision happens at the contact point, so its speed — not the COM speed — decides whether the bodies approach.
Step 4 · Velocity of a Point on a Rigid Body
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
9

## Slide 10
A collision force is huge and brief — integrate it once and change the velocity in a jump
Linear and angular impulse–momentum
Worked example (T: )
N·s at m : m/s, rad/s
pusht_keyboard_sim.py : resolve_impulse
J = j_n * n
body.vel += J / body.mass
body.omega += cross2(r, J) / body.inertia
# back to a force for display (advance):
F = self._j_sum / (n * self.physics_dt)
Why jump : the contact lasts milliseconds, positions barely move, and the force history is unknown — only its integral matters.
Step 5 · Impulse: A Large Force for a Short Time
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
10

## Slide 11
Start with a particle hitting a wall, then let the body rotate
Restitution law (normal direction)
Particle:
Rigid body: rotation absorbs part of it
After impact
1
elastic: full bounce
0.5
half the approach speed
0
plastic: no bounce (PushT)
resolve_impulse
K_n = 1.0 / body.mass \
+ cross2(r, n) ** 2 / body.inertia
j_n = -(1.0 + restitution) * v_n / K_n
Same formula : becomes , the "effective inverse mass" seen at the contact — derived in full a few slides later.
Step 6 · A Collision: How Big Is the Impulse?
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
11

## Slide 12
Every rigid-body simulator repeats the same five stages in each time step
Forces
PD, damping
Integrate
Steps 1–3
Detect
who touches whom
Impulse
Steps 4–6
Correct
remove overlap
Stage
PushT
Code
Forces
PD pusher toward the target; floor damping on the T
substep, steps 1–2
Integrate
semi-implicit Euler for pusher and T
substep, step 3
Detect
circle vs. T polygon; T corners vs. walls
circle_vs_T, wall_contacts
Impulse
normal with , Coulomb friction
resolve_impulse
Correct
push the T out of any overlap
end of resolve_impulse
Next : the following slides open each stage of the PushT code and put the equations beside it.
Step 7 · A Simulation Loop with Contacts
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
12

## Slide 13
One env.step() = 0.1 s = 20 substeps of 5 ms, each with a 3-pass contact solver
Target
PD pusher
Contact
point, , depth
Impulse
T motion
Time steps
Average contact force
pusht_imitation.py : PushTEnv.step · pusht_keyboard_sim.py : advance
def step(self, action):
self.sim.target = np.clip(action, [x_min, y_min], [x_max, y_max])
self.sim.advance(self.control_dt) # 0.1 s
self.t += 1
def advance(self, frame_dt):
n = max(1, int(round(frame_dt / self.physics_dt)))
self._j_sum[:] = 0.0
for _ in range(n):
self.substep(self.physics_dt) # 5 ms
F = self._j_sum / (n * self.physics_dt) # impulse / time
Physics Inside One Control Step
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
13

## Slide 14
The pusher is a controlled kinematic body; the T coasts and slows down by floor friction
1. PD control of the pusher
: damping ratio — fast, no overshoot. Speed limited to m/s.
2. Floor friction as exponential decay
3. Semi-implicit Euler
pusht_keyboard_sim.py : KeyboardPushT.substep
# 1. pusher PD control toward the target
acc = self.kp * (self.target - P.pos) - self.kd * P.vel
P.vel += acc * dt
speed = np.linalg.norm(P.vel)
if speed > self.max_speed:
P.vel *= self.max_speed / speed
P.pos += P.vel * dt # new velocity first
# 2. damping 3. integrate the T
T.vel *= math.exp(-self.linear_damping * dt)
T.omega *= math.exp(-self.angular_damping * dt)
T.pos += T.vel * dt
T.angle += T.omega * dt
Consequence : released at speed , the T slides another — the expert slows down near the goal for this reason.
Substep: PD Pusher, Damping, Integration
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
14

## Slide 15
Composite body: two rectangles, each shifted to the T's centre of mass
Centre of mass (mass ∝ area)
Rectangle + parallel-axis theorem
Value ()
Result
top bar
stem
COM below the top edge
0.627
0.434
pusht_keyboard_sim.py : make_T_geometry
top_area = W * top_t
stem_h = H - top_t
stem_area = stem_w * stem_h
total_area = top_area + stem_area
y_top, y_stem = H / 2 - top_t / 2, -top_t / 2
y_com = (top_area * y_top + stem_area * y_stem) / total_area
m_top = mass * top_area / total_area
m_stem = mass * stem_area / total_area
# own centre + parallel-axis shift to the COM
I_top = m_top * (W**2 + top_t**2) / 12 \
+ m_top * (y_top - y_com) ** 2
I_stem = m_stem * (stem_w**2 + stem_h**2) / 12 \
+ m_stem * (y_stem - y_com) ** 2
vertices[:, 1] -= y_com # body origin = COM
T Geometry: Mass Moment of Inertia
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
15

## Slide 16
Work in the T's own frame: closest point on the 8 edges, then inside / outside
World → body frame
Closest point on edge
Penetration (pusher radius )
pusht_imitation.py : circle_vs_T_fast (all edges at once)
R = rotation_matrix(body_angle)
c = R.T @ (circle_pos - body_pos) # world -> T
A = vertices
AB = np.roll(vertices, -1, axis=0) - A
t = np.clip(((c - A) * AB).sum(1) / (AB * AB).sum(1), 0, 1)
Q = A + t[:, None] * AB # closest points
d2 = ((Q - c) ** 2).sum(1)
i = int(np.argmin(d2))
d = math.sqrt(d2[i])
inside = ... # ray casting
if not inside and d >= radius:
return None
direction = (Q[i] - c) / d
n_local, pen = (-direction, radius + d) if inside \
else (direction, radius - d)
n = R @ n_local
return body_pos + R @ Q[i], n, pen
Speed : the numpy version replaces an 8-iteration Python loop — identical results on 2000 random cases, checked in the tutorial.
Contact Detection: Circle vs T
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
16

## Slide 17
Relative velocity says whether the bodies approach; an impulse stops them
Velocity of the contact point
Normal impulse
pusht_keyboard_sim.py : resolve_impulse (part 1)
point, n, pen = contact
r = point - body.pos
v_rel = body.vel + omega_cross_r(body.omega, r) - other_vel
v_n = float(np.dot(v_rel, n))
if v_n < 0: # approaching
K_n = 1.0 / body.mass + cross2(r, n) ** 2 / body.inertia
j_n = -(1.0 + restitution) * v_n / K_n
J = j_n * n
body.vel += J / body.mass
body.omega += cross2(r, J) / body.inertia
def cross2(a, b): # 2D cross product, z only
return a[0] * b[1] - a[1] * b[0]
Kinematic pusher : , so only the T's terms remain in . PushT uses — after impact .
Contact Velocity and Normal Impulse
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
17

## Slide 18
The same push at a different height splits into translation and rotation differently
Derivation: normal velocity change at C
Stem's left face (), , :
Height
0 (COM)
1.000
1.000
1.000
0.000
−0.5
1.576
0.634
0.634
0.731
−1.0
3.305
0.303
0.303
0.697
Output of resolve_impulse() — pusht_mini_sim.py, section 8
At the COM : pure translation. Far from the COM : smaller impulse, mostly rotation.
This is PushT : choosing the contact point chooses the motion — exactly what the scripted expert and the learned policies must do.
Why Contact Height Matters
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
18

## Slide 19
Cancel the sliding velocity at the contact, but never beyond
Tangent direction
Impulse that stops sliding
Coulomb limit
pusht_keyboard_sim.py : resolve_impulse (part 2)
# friction, using the velocity after the normal impulse
t = np.array([-n[1], n[0]])
v_rel = body.vel + omega_cross_r(body.omega, r) - other_vel
v_t = float(np.dot(v_rel, t))
K_t = 1.0 / body.mass + cross2(r, t) ** 2 / body.inertia
j_t = float(np.clip(-v_t / K_t,
-friction * j_n, friction * j_n))
Jt = j_t * t
body.vel += Jt / body.mass
body.omega += cross2(r, Jt) / body.inertia
Effect : with friction the pusher can drag the T sideways and rotate it; with it slips along the surface (try F in the keyboard demo).
Coulomb Friction Impulse
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
19

## Slide 20
A wall is a kinematic body with zero velocity — the same impulse function handles it
Wall = pusher with
Left wall:
Penetration correction
Discrete time jumps leave overlaps that impulses alone cannot remove.
pusht_keyboard_sim.py : wall_contacts · substep (step 4)
world = body.pos + body.vertices @ rotation_matrix(body.angle).T
for p in world:
for depth, n in ((x_min - p[0], (1.0, 0.0)), ...):
if depth > 0:
contacts.append((p.copy(), np.array(n), depth))
# 4. contact solver: pusher-T and wall-T
for _ in range(3):
c = circle_vs_T(P.pos, P.radius, T.pos, T.angle, T.vertices)
if c is not None:
jn, jt = resolve_impulse(T, P.vel, c, e, mu)
for w in wall_contacts(T):
resolve_impulse(T, np.zeros(2), w, e, mu)
# end of resolve_impulse
body.pos += 0.8 * max(pen - 1e-4, 0.0) * n
Walls and Penetration Correction
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
20

## Slide 21
Every line of the simulator is an equation from the dynamics lecture
Lecture idea
Equation
Code
PD control
substep, step 1
Parallel-axis theorem
make_T_geometry
Relative velocity
omega_cross_r
Restitution
j_n = -(1+e) v_n / K_n
Linear impulse–momentum
body.vel += J / m
Angular impulse–momentum
body.omega += cross2(r, J) / I
Coulomb friction
np.clip(-v_t / K_t, ...)
Impulse = force × time
advance
Files : derivations in pusht_mini_sim.py · real-time version in pusht_keyboard_sim.py · random tasks in pusht_imitation.py
Physics Summary: Equation ↔ Code
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
21

## Slide 22
A policy maps what the agent observes to what it does — here every 0.1 s
Observation
from the state
Policy
Action
pusher target
Physics
next state
Policy
How it decides
In this course
Human
eyes + experience
keyboard recorder
Scripted
hand-written rules from physics
ScriptedExpert
Neural network
learned weights
MLP-BC, Diffusion, PPO actor
Closed loop : the policy sees the result of its last action, so it can correct its own mistakes.
Deterministic vs. stochastic : or — the second is needed for multimodal demos and for RL exploration.
Step 8 · What Is a Policy?
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
22

## Slide 23
python pusht_imitation.py collect — the keyboard simulator with a recorder added
Recorder window: arrows / WASD or mouse drag move the target; reaching the goal auto-saves
Three rules for clean data
Fixed 10 Hz : the screen draws at 20 fps, but is recorded every 0.1 s — one human step = one env.step().
Idle start trimmed : time spent thinking before the first move is not recorded, so the policy never learns to stand still.
Physics fixed : friction / restitution switches are off — same state, same consequence.
Keys : N new task · R restart · Backspace delete last · Space pause
Cost : one human demo takes 15–30 s, so 200 demos take 1.5–2 hours → we also need an automatic demonstrator.
Collecting Human Demonstrations
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
23

## Slide 24
A "virtual human" that chooses where to push with the lecture's impulse equations
(1) Where to push — unit impulse at candidate
Candidates : 8 edges × 3 points; = desired , = its effect.
(2) Approach : go to a standoff point; orbit around the T if the straight path is blocked.
(3) Push : along , slowing in proportion to the remaining error (the T slides after release).
Expert rollouts (orange: pusher path, colour: time) — success ≈ 88–91 % on random tasks
Scripted Expert: Impulse–Momentum as a Policy
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
24

## Slide 25
Score each candidate push by how well its impulse response points toward the goal
Desired change ()
Response to a unit impulse at
Cosine score
Penalty for pushing into a touching wall; +0.1 for keeping the same contact.
pusht_imitation.py : ScriptedExpert.act
e = sim.goal_pos - T.pos
d = np.array([e[0], e[1],
self.L * wrap_angle(sim.goal_angle - T.angle)])
for k, (c_local, out_local) in enumerate(self.cands):
cw, out = T.pos + R @ c_local, R @ out_local
n_in, r = -out, cw - T.pos
c = np.array([n_in[0] / T.mass, n_in[1] / T.mass,
self.L * cross2(r, n_in) / T.inertia])
score = c @ d / (np.linalg.norm(c) * d_norm + 1e-9)
for n_wall in walls:
if n_in @ np.array(n_wall) < -0.3:
score -= 0.6 # into that wall
if k == self.cur:
score += 0.1 # hysteresis
# push: slower when close to the goal
step = float(np.clip(0.3 * d_norm, 0.04, 0.12))
return P.pos - out * (step + 0.04)
Scripted Expert: Equation ↔ Code
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
25

## Slide 26
Published PushT and manipulation work uses 50–200 demonstrations per task
Source
Task
Demonstrations
Diffusion Policy (Chi et al., 2023)
PushT, fixed goal, random start
200 human (≈ 25k steps)
LeRobot pusht dataset
same task
206 episodes, 25,650 frames
ACT / ALOHA (Zhao et al., 2023)
real bimanual robot
50 per task
Suggested plan for human demonstrations (15–30 s each)
Stage
Demos
Time
Purpose
Pipeline check
10–20
10 min
save / load / train runs, loss goes down
First results
50–100
30–60 min
successes start; study the failures
Usable policy
≥ 200
1.5–2 h
Diffusion Policy paper scale
More important than the count : spread-out initial conditions, a consistent strategy, and discarded failures. Our goal is random too — harder than the original PushT.
How Many Demonstrations? Reference Points
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
26

## Slide 27
Ride along with the goal — the same idea as relative motion in rigid-body kinematics
Action representation (goal frame)
MLP-BC
Diffusion
absolute target position
26 %
20 %
offset from the current pusher
36 %
46 %
One training sample: goal at the origin, 0°
Without the goal frame : 0 % success for both models — a good representation saves data.
Goal Frame: Relative Motion Removes the Random Goal
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
27

## Slide 28
A rotation and a translation — written out by hand so it works on any batch shape
State layout: → indices 0–7.
pusht_imitation.py : to_goal_frame · make_obs · action_to_model
def to_goal_frame(points, state, origin=None):
c, s = math.cos(state[7]), math.sin(state[7])
v = points - (state[5:7] if origin is None else origin)
return np.stack([ c * v[..., 0] + s * v[..., 1],
-s * v[..., 0] + c * v[..., 1]], -1)
def make_obs(state):
p = to_goal_frame(state[0:2], state)
T = to_goal_frame(state[2:4], state)
dth = state[4] - state[7]
return np.array([p[0], p[1], T[0], T[1],
math.cos(dth), math.sin(dth)])
def action_to_model(actions, state):
return to_goal_frame(actions, state, origin=state[0:2])
Goal Frame: Equation ↔ Code
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
28

## Slide 29
See two frames, plan eight actions, execute four, then re-plan
Observe
,
Predict
, (0.8 s)
Execute
first actions
Re-plan
receding horizon
Two frames : the difference gives velocity — is the T still sliding?
Chunks : one-step predictions change every 0.1 s and jitter; a chunk commits to a motion for a moment.
Normalize : , statistics from the training set only.
Split by episode : neighbouring steps are nearly identical — a step-wise split leaks data into validation.
Trade-off : 4 steps run open-loop, so an unexpected slide is corrected only at the next re-plan.
Observation History and Action Chunks
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
29

## Slide 30
Fit a function to examples by following the gradient of a loss
Loss on a minibatch of examples
Gradient descent
Minibatch , drawn at random every step. AdamW adapts the step per parameter. Validation set : episodes never trained on.
pusht_imitation.py : train
opt = torch.optim.AdamW(model.parameters(), lr=lr)
sched = CosineAnnealingLR(opt, steps)
for it in range(1, steps + 1):
idx = torch.randint(0, len(X), (batch,))
loss = model.loss(X[idx], Y[idx])
opt.zero_grad()
loss.backward() # gradient
opt.step() # phi <- phi - lr * ...
sched.step() # lr decays to 0
Loss ≠ goal : a low loss on demos does not guarantee success in closed loop — that is why every model here is evaluated by running it.
Step 9 · Supervised Learning in One Slide
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
30

## Slide 31
Stack linear maps and nonlinearities; the weights are what training changes
MLP-BC in PushT
Size
input
2 × 6 = 12
hidden layers
3 × 512
output (8 actions × 2)
16
parameters
540,176
pusht_imitation.py : MLP · BCPolicy
class MLP(nn.Module):
def __init__(self, d_in, d_out, width=256, depth=3):
layers, d = [], d_in
for _ in range(depth):
layers += [nn.Linear(d, width), nn.Mish()]
d = width
self.net = nn.Sequential(*layers, nn.Linear(d, d_out))
class BCPolicy(Normalized):
def loss(self, x, y): # MSE, normalized
return ((self.f(self.nx(x)) - self.ny(y)) ** 2).mean()
Why a nonlinearity : without the whole stack collapses into one linear map — it could not represent "push left of the T here, right of it there".
Step 10 · The Network: A Multi-Layer Perceptron
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
31

## Slide 32
Behavior cloning = supervised learning with observation and expert action
Covariate shift
Training states come from the expert; at test time states come from the policy itself. One small error leads to a state the demos never showed, where the next error is larger.
Ross & Bagnell (2010); Ross, Gordon & Bagnell (2011)
Two more problems
Multimodality : the MSE optimum is the mean of the demonstrated actions (next slides).
No recovery data : we save only successful demos, so the policy never sees how to fix a bad push.
Remedies in this course : action chunks, Diffusion Policy for multimodality — and RL fine-tuning, which learns from the policy's own states.
Step 11 · Behavior Cloning and Its Weak Spot
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
32

## Slide 33
MSE learns the average action — the average of two good actions can be bad
Toy problem: demonstrations avoid an obstacle up or down (50/50). MLP-BC learns — straight into it; Diffusion samples both modes.
In PushT : "go around the left or the right side of the T?" — MLP-BC hesitates in between; human demos are even more multimodal.
Which Model? The Multimodality Problem
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
33

## Slide 34
Learn a distribution instead of a single average action
Model
Output
Multimodal
Notes
MLP-BC (MSE)
one point
no (mean)
fastest, simplest — baseline
MLP-BC + action chunk
points
no
temporally consistent
GMM / MDN
Gaussians
partly
number of modes fixed in advance
VQ-BeT
discrete code + offset
yes
Transformer
ACT (CVAE + Transformer)
chunk
yes
real robot, 50 demos
Diffusion Policy
chunk, sampled
yes
standard PushT baseline, stable training
Our choice : MLP-BC as the baseline, Diffusion Policy as the main model — same MLP trunk (3 layers, width 512, Mish).
So the only difference is : learning the mean vs. learning the distribution.
Policy Model Candidates
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
34

## Slide 35
Learn to remove noise from action chunks; at run time, denoise noise into actions
1. Forward process: mix noise into a clean chunk
2. Training: predict the noise
3. Sampling: start from , step
Why it is multimodal : each run starts from different noise → a different sample → different modes of the demonstrations. Cosine schedule , .
Diffusion Policy (DDPM) in Three Steps
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
35

## Slide 36
Training is one line of noise mixing; sampling is a loop of K = 50 denoising steps
Training
Sampling
pusht_imitation.py : DiffusionPolicy.loss · predict
def loss(self, x, y):
a0 = self.ny(y)
k = torch.randint(0, self.K, (len(a0),))
eps = torch.randn_like(a0)
ab = self.abar[k][:, None]
a_k = ab.sqrt() * a0 + (1 - ab).sqrt() * eps
return ((self.eps_hat(a_k, k, self.nx(x)) - eps) ** 2).mean()
def predict(self, x):
a = torch.randn(len(xn), self.d_act) # a^K ~ N(0, I)
for k in reversed(range(self.K)):
ab = self.abar[k]
a0 = (a - (1 - ab).sqrt() * self.eps_hat(a, kk, xn)) / ab.sqrt()
mean = (ab_prev.sqrt() * self.betas[k] / (1 - ab)) * a0 \
+ (self.alphas[k].sqrt() * (1 - ab_prev) / (1 - ab)) * a
var = self.betas[k] * (1 - ab_prev) / (1 - ab)
a = mean + var.sqrt() * torch.randn_like(a)
Diffusion Policy: Equation ↔ Code
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
36

## Slide 37
Diffusion needs more capacity or more steps than MLP-BC before it pays off
Setting (180 expert demos, unseen tasks)
MLP-BC
Diffusion
width 256, lr , no EMA, 30k steps
32 %
8 %
width 256, lr + EMA, 30k steps
36–46 %
18–42 %
width 256, lr + EMA, 80k steps
—
64 %
width 512, lr + EMA, 30k steps (default)
38–59 %
54–63 %
width 512, lr + EMA, 50k steps
—
69 %
Batch 256, AdamW, cosine lr decay; about 1 min per model on GPU, 4 min on CPU.
Caution : re-running the same setting moves success by ±10 %; validation loss does not predict success (0.116 → 0.132 while 62 % → 69 %).
Training Settings Found by Experiment
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
37

## Slide 38
Diffusion reaches most of its performance at about 100 demonstrations
Experiment
400 expert demos → train on the first → width 512, 30k steps → 100 unseen tasks, closed loop.
Reading
Diffusion is ahead at every , most clearly with little data.
MLP-BC needs about 3× more demos for the same success.
Human demos : aim for at least 100, ideally 200.
Reproduce : tools/imitation_experiments/full/run_scale512.sh (10 jobs, about 15 min)
How Many Demonstrations? Measured
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
38

## Slide 39
Both learned policies stay below the expert that taught them
MLP-BC rollouts on unseen seeds
Diffusion Policy rollouts on the same seeds
MLP-BC : stalls or jitters beside the T — it averages between strategies.
Diffusion : commits to one strategy; fails at the final 0.15 m / 10° alignment or after one big mistake.
Both : covariate shift — their own errors lead to states never seen in the demos.
Default run (180 demos) : expert 88 % · MLP-BC 38–59 % · Diffusion 54–63 %. Remedy: DAgger — record human corrections.
Closed-Loop Rollouts and Failure Modes
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
39

## Slide 40
No teacher — the agent acts, and the environment answers with a new state and a reward
Agent
policy
Environment
the simulator (Steps 1–7)
Feedback
Markov decision process for PushT
Element
PushT
state
pusher, T and goal poses (+ velocities)
action
where to move the pusher target
transition
0.1 s of physics — deterministic here
reward
progress toward the goal, bonus on success
episode
until success or 300 steps (30 s)
Markov property : the next state depends only on — that is why velocities belong in the state, or two frames in the observation.
Step 12 · The RL Problem: Learning from Reward
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
40

## Slide 41
The agent maximizes the discounted sum of rewards, not the next reward
Value
effective horizon
100 steps = 10 s
bonus 10 after 100 steps
bonus 10 after 50 steps
Discounting : a success that comes sooner is worth more — together with the −0.01 time penalty, this is why RL learns to finish faster than the expert.
: one trajectory produced by running the policy.
Step 13 · Return: Adding Up Future Rewards
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
41

## Slide 42
How good is a state? The return the policy can expect from there
Bellman equation (from )
Temporal-difference (TD) error
: the step went better than the critic expected.
pusht_rl.py : critic
# the critic V_psi(s) is another network
# trained by regression on the returns:
lv = ((model.value(Ob[idx]) - RET[idx]) ** 2).mean()
# TD error inside GAE
delta = R[t] + gamma * nv * (1 - DONE[t]) - V[t]
Episode end : after success — no future value. A time-out is not an end, so is added back (bootstrap).
Step 14 · Value Function and Bellman Equation
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
42

## Slide 43
Was this action better or worse than what the policy usually does in this state?
Generalized Advantage Estimation
Estimate
0
one-step TD: low variance, biased by the critic
1
full return − : unbiased, noisy
0.95
the usual compromise (used here)
pusht_rl.py : GAE
for t in reversed(range(n_steps)):
nv = v_next if t == n_steps - 1 else V[t + 1]
delta = R[t] + gamma * nv * (1 - DONE[t]) - V[t]
g = delta + gamma * lam * (1 - DONE[t]) * g
adv[t] = g
RET = ADV + torch.cat(V) # critic target
ADV = (ADV - ADV.mean()) / (ADV.std() + 1e-8)
Step 15 · Advantage and GAE
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
43

## Slide 44
Make better-than-usual actions more likely, and worse-than-usual ones less likely
Gaussian policy for continuous actions
Policy-gradient theorem
: move toward the tried action. : move it away.
pusht_rl.py
def policy_dist(model, o):
return torch.distributions.Normal(
model.mean(o), model.log_std.exp())
# training: sample -> exploration
# evaluation: use model.mean(o)
Compare with BC : BC pulls toward the expert's action; policy gradient pulls it toward the agent's own actions, weighted by how well they worked.
Step 16 · Policy Gradient
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
44

## Slide 45
Reuse each batch for several updates — but never move the policy too far at once
At its gradient is exactly the policy gradient of Step 16.
Case
Effect of the clip ()
stop raising the probability once
stop lowering it once
1. Collect
64 envs × 128 steps
2. GAE
, returns
3. Update × 10 epochs
actor + critic MSE
4. Repeat
Why the clip : one bad, too-large update can destroy a policy that works — critical when we start from the BC policy.
Step 17 · From Policy Gradient to PPO
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
45

## Slide 46
RL can only improve what it has tried — success has to happen at least sometimes
Sparse vs. shaped reward
Sparse : +10 only at success. A random pusher practically never aligns the T within 0.15 m and 10° → no learning signal.
Shaped : every step. Potential-based, so the best policy is unchanged (Ng et al., 1999).
What we measured
Start
Before
After PPO
random
0 %
0 % (16.4M steps)
BC policy
42 %
80–82 % (6M)
From scratch the return rose −14 → −2.4: the T moved closer, but the final alignment was never discovered.
Key idea : demonstrations solve exploration; RL then optimizes the reward. Imitation and RL are complementary, not competitors.
Step 18 · Exploration and Reward Shaping
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
46

## Slide 47
RL needs no demonstrations — only a reward and a great deal of trial and error
Experiment
Starting point
Result (50 unseen tasks, no exploration noise)
A. RL from scratch
random network
16.4M steps (2.5 h): 0 % success
B. BC → RL
MLP-BC policy
42 % → 74 % (3M) → 80 % (6M, 80 min)
Scripted expert
hand-written rules
88 %
Why A fails : success needs a long sequence — choose a contact, go around, push, align. Random motion almost never completes it, so the success bonus is never observed (the exploration problem).
Why B works : imitation already succeeds about half the time; RL only has to polish behaviour that works.
From Imitation to Reinforcement Learning
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
47

## Slide 48
Turn "how far is the task from done" into one number, and reward every step of progress
Remaining cost (1 rad ≈ 0.3 m)
Reward per step
Potential-based shaping : the progress term sums to — a signal every step, without changing the optimal policy.
Episode end : success is terminal; at 300 steps it is truncated and bootstrapped with .
Side effect : the time penalty makes RL finish faster than the expert, which has no such pressure.
Reward Design
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
48

## Slide 49
Two short functions — the RL training loop calls them once per environment step
: positive when the T moved closer to the goal pose.
wrap_angle keeps in , so counts as .
pusht_rl.py : task_cost · reward
def task_cost(sim):
return float(np.linalg.norm(sim.T.pos - sim.goal_pos)
+ 0.3 * abs(wrap_angle(sim.T.angle - sim.goal_angle)))
def reward(c_before, c_after, sim, success):
dist_pt = float(np.linalg.norm(sim.pusher.pos - sim.T.pos))
return (10.0 * (c_before - c_after)
- 0.02 * max(dist_pt - 1.0, 0.0)
- 0.01
+ (10.0 if success else 0.0))
Reward: Equation ↔ Code
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
49

## Slide 50
Collect 8,192 steps, estimate advantages, update for 10 epochs — repeat
Advantage (GAE),
Clipped objective,
Gaussian policy : sample while training, use the mean for evaluation.
A. scratch
B. BC → RL
Actor
2 × 256 tanh
the MLP-BC net
Initial
0.6
0.03 m
Actor lr
Critic
new
new, 10 warm-up updates
For B : clipping, a small learning rate and small noise protect the working BC policy from being destroyed early on.
PPO: Small, Clipped Policy Updates
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
50

## Slide 51
GAE runs backwards through the rollout; the clipped loss is one line
Advantage, backwards in time
Clipped surrogate
pusht_rl.py : train loop
for t in reversed(range(n_steps)): # GAE
nv = v_next if t == n_steps - 1 else V[t + 1]
delta = R[t] + gamma * nv * (1 - DONE[t]) - V[t]
g = delta + gamma * lam * (1 - DONE[t]) * g
adv[t] = g
RET = ADV + torch.cat(V) # critic target
for _ in range(10): # PPO epochs
...
lv = ((model.value(Ob[idx]) - RET[idx]) ** 2).mean()
if it >= critic_warmup:
ratio = (policy_dist(model, Ob[idx]).log_prob(Ab[idx])
.sum(-1) - LPb[idx]).exp()
la = -torch.min(ratio * ADV[idx],
ratio.clamp(0.8, 1.2) * ADV[idx]).mean()
PPO: Equation ↔ Code
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
51

## Slide 52
Pure-Python physics is slow, so 64 environments run at once on 16 CPU processes
Main process
policy for 64 observations at once
16 workers × 4 envs
physics, auto-reset on done
Benchmark (idle CPU, 20 cores)
Steps per PPO iteration
64 × 128 = 8,192
Rollout (physics 3.09 s)
3.79 s
PPO update
1.91 s (33 %)
Env steps / s
2,159 rollout · 1,437 total
Training wall-clock (from logs)
Run
Steps
Time
RL from scratch
16.4M
147 min
BC+PPO
0 → 6M
80 min
BC+PPO resumed
6 → 12M
70 min
Backend : CPU multiprocessing (fork + Pipe); the network also runs on the CPU. One environment alone would be ≈ 64× slower.
Parallel Simulation
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
52

## Slide 53
Starting from imitation turns an unsolvable exploration problem into fine-tuning
Training success with exploration noise (tutorial/checkpoints/rl/*/train_log*.txt)
From scratch : return improved −14 → −2.4, the T moves toward the goal, but 0 % success; exploration noise collapsed 0.6 → 0.03.
BC → RL : 0.44 → 0.88 in 6M steps, then a plateau at 0.87–0.90.
Lesson : demonstrations solve exploration; RL then optimizes what imitation cannot — the reward itself.
RL from Scratch vs BC → RL
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
53

## Slide 54
Same 100 unseen tasks, same start, 300 steps, deterministic actions for every policy
pusht_rl_eval.py → tutorial/eval_results/paired_*.csv / .json
Scripted vs BC+PPO
6M
12M
both succeed
74
70
only scripted
13
17
only BC+PPO
8
7
both fail
5
6
McNemar
0.38
0.064
median steps*
136 → 107
139 → 104
* on seeds both solved: scripted → BC+PPO
Result : success is statistically tied with the expert, and BC+PPO is about 3–4 s faster on the same tasks.
Paired Evaluation on Seeds 0–99
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
54

## Slide 55
More training made the policy faster, not more successful
Measured
Within noise : at 82 %, one standard error is about ±4 points with 100 tasks.
6M → 12M : success 82 % → 77 %, mean time 12.0 s → 11.1 s.
Plateau : training success stayed at 0.87–0.90 with noise .
Best checkpoint : 6M, not the newest 12M.
Likely structural limits (not yet tested)
Less information : 12 inputs vs. the expert's full state and memory.
Conservative updates : lr , clipping, small .
Reward ≠ success test : angle weighted 0.3; success needs 0.15 m and 10°.
One step at a time : BC drops 54 % → 34 % without chunks.
Not a ceiling : RL optimizes the reward, not imitation — align the reward with the success test to push further.
Why BC+PPO Stops Near the Expert
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
55

## Slide 56
python pusht_rl_realtime.py — every panel replays the same random task live
Seed 30: script 8.7 s · BC→RL 6.4 / 6.2 s · BC and RL-from-scratch time out
Run
cd tutorial
python pusht_rl_realtime.py
python pusht_rl_realtime.py script
python pusht_rl.py eval
python pusht_rl_eval.py
Keys
Space pause · N next task · + / − speed · Q quit
Real-Time Demo: Five Policies, One Task
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
56

## Slide 57
From to a policy that beats the expert's speed
Steps
Idea
Where in the code
1–3
Newton in discrete time, damping, rigid-body pose
substep, TBody
4–6
contact-point velocity, impulse, restitution,
resolve_impulse
7
simulation loop with contact detection
circle_vs_T, wall_contacts
8–11
policy, supervised learning, MLP, behavior cloning
BCPolicy, train
—
multimodality → Diffusion Policy
DiffusionPolicy
12–15
MDP, return, value, advantage (GAE)
pusht_rl.py: reward, GAE
16–18
policy gradient, PPO, exploration
pusht_rl.py: PPO loop
Result : scripted 87 % · BC 54 % · BC+PPO 82 % on the same 100 unseen tasks — tied with the expert in success, 3–4 s faster.
The Whole Chain, Step by Step
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
57

## Slide 58
•
Imitation learning = supervised learning on from successful demonstrations
→
Goal frame (relative motion) and action offsets matter as much as the model
•
Data: about 100 demos for Diffusion Policy; collect 100–200 human demos
•
Model: MSE learns ; Diffusion learns the distribution and handles multimodality
→
Measured: Diffusion 20–68 % vs MLP-BC 9–59 % (25–360 demos)
•
RL from scratch: 0 % after 16M steps — the exploration problem
→
BC → PPO: 54 % → 82 % on seeds 0–99, tied with the expert (87 %) and 3–4 s faster
Physics gives the data, imitation gives the start, RL gives the polish
Summary
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
58

## Slide 59
•
Human data : collect 50, then 100 demos — does the Diffusion vs MLP-BC gap grow?
•
No goal frame : train in world coordinates — how much success is lost?
•
Chunks : vary the prediction / execution horizons (1, 4, 8, 16)
•
History : one observation frame — which mistakes appear without velocity?
•
DAgger : record your corrections in the viewer and retrain
•
Robustness : evaluate with friction 0.2 instead of 0.4 — think domain randomization
•
RL : put the 0.15 m / 10° test into the reward — does BC+PPO pass the expert?
Exercises with the tutorial code
Try It Yourself
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
59