## Slide 1
Simulating a Digital Twin:
Spring–Mass Model and Frictional Contact
Department of Mechanical Engineering
Advanced Deep Learning 2026
Joo Yong Sim
PhysTwin and real2sim-eval read line by line — with measurements from our own experiments on a rope

## Slide 2
A digital twin is a physics model that a robot can push, grasp and learn on
Observation
3 RGB-D cameras
Particles
+ spring graph
Physics
springs · contact · ground
Robot learning
teleop · RL · evaluation
Three questions for this lecture
Q1 — Simulation model : how does a cloud of particles behave like a rope? (springs, dashpots, drag, integrator)
Q2 — Contact model : how do the ground, the rope itself and a robot gripper push back — and how is friction written?
Q3 — Cost and consequences : what makes it slow, and what does contact do to repeatability and learning?
Sources : PhysTwin (arXiv 2503.17973) · real2sim-eval (arXiv 2511.04665) · our projects 13–21 on the released rope twin
Lecture Goals: From Video to a Simulator
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
2

## Slide 3
Same particles and springs; they differ in how the hand or gripper touches the object
PhysTwin
real2sim-eval
Purpose
fit physics to a video (system ID)
evaluate robot policies
Hand / gripper
control points welded by springs
finger triangle mesh, frictional contact
Can the object slip or drop?
no — the springs never release
yes — held only by friction
Gradients
differentiable (Warp tape)
forward only, overwritten in place
Self-collision distance
0.02 m (off for real data)
0.005 m (on)
Time step
s, substeps per 30 fps frame (both)
Rope twin (rope_0001)
2,002 particles · 17,048 object springs · 514 mm long · 31.5 mm across
real2sim-eval §III-C : “we avoid the common but unrealistic practice of fixing object nodes to the gripper.” Everything about contact in this lecture follows from that choice.
Two Simulators, One Spring Network
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
3

## Slide 4
Every particle has ; springs join neighbours found at frame 0
Neighbour search (KD-tree)
Defaults m, ; the released rope uses mm, .
Rest length — frozen at frame 0
Rope particles
Count
tracked (from video)
1,495
surface + interior (filled)
288 + 219
median spacing
3.06 mm
PhysTwin qqtt/engine/trainer_warp.py : spring construction
pcd_tree = o3d.geometry.KDTreeFlann(object_pcd)
for i in range(len(points)):
[k, idx, _] = pcd_tree.search_hybrid_vector_3d(
points[i], object_radius, object_max_neighbours)
for j in idx[1:]:
rest = np.linalg.norm(points[i] - points[j])
if (i, j) not in seen and rest > 1e-4:
springs.append([i, j])
rest_lengths.append(rest)
masses = np.ones(len(points)) # all particles m = 1
# repeat 2 (projects 17, 21): 4,004 particles,
# 34,090 springs; scaling tests up to 100,100
State and the Spring Graph
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
4

## Slide 5
Hooke's law on strain plus a dashpot along the spring — equal and opposite on the two ends
Unit direction and strain
Spring + axial dashpot
multiplies a strain, so it acts like , not N/m. Dashpot .
real2sim-eval sim/physics/spring_mass_warp.py : eval_springs
tid = wp.tid() # one thread per spring
if wp.exp(spring_Y[tid]) > spring_Y_min:
dis = x2 - x1
dis_len = wp.length(dis)
d = dis / wp.max(dis_len, 1e-6)
spring_force = (
wp.clamp(wp.exp(spring_Y[tid]),
low=spring_Y_min, high=spring_Y_max)
* (dis_len / rest - 1.0) * d)
v_rel = wp.dot(v2 - v1, d)
dashpot_forces = dashpot_damping * v_rel * d
overall_force = spring_force + dashpot_forces
wp.atomic_add(f, idx1, overall_force)
wp.atomic_sub(f, idx2, overall_force)
Note the atomics : many springs add into the same particle in parallel — the summation order is not fixed (we return to this at the end).
Spring–Dashpot Force on Each Edge
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
5

## Slide 6
One stiffness per spring, optimised in log space and clamped to a range
Parameterisation
Why log : for free, and a gradient step changes by a ratio, not an amount. Initial .
Trap : case.spring_Y is linear, sim.wp_spring_Y is its log — exponentiate the wrong one and every spring sits at the clamp.
float32 : cancels near 1 — 2.3 % force error vs float64.
Fitted stiffness, rope_0001
Quantile
min
11.5
p10
1,821
median
43,785
p90
100,797
max
102,244
p10–p90 spread 55× here vs 1.05× in PhysTwin's single_push_rope — many springs ride the upper clamp.
Stiffness Is Stored as a Logarithm
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
6

## Slide 7
Velocity first from forces, then position from the new (contact-corrected) velocity
1. Velocity from force, then drag
s : exponential decay, never overshoots zero.
2. Contacts modify
3. Position (symplectic Euler)
spring_mass_warp.py : update_vel_from_force
tid = wp.tid() # one thread per particle
v0 = v[tid]
f0 = f[tid]
m0 = masses[tid]
drag_damping_factor = wp.exp(-dt * drag_damping)
all_force = f0 + m0 * wp.vec3(0.0, 0.0, -9.8) \
* reverse_factor # PhysTwin: z down
a = all_force / m0
v1 = v0 + a * dt
v2 = v1 * drag_damping_factor
v_new[tid] = v2
Upstream quirk : with a mesh present, mesh_collision already writes and the ground kernel advances again — free fall measured at 2.002× analytic. The released parameters were fitted with it.
Gravity, Drag and Semi-Implicit Euler
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
7

## Slide 8
An explicit integrator must resolve the fastest spring — the stiffest, shortest one
One spring, one mass:
Symplectic Euler is stable for
with , shortest mm. The dashpot limit ms is far looser.
Released s sits within 1.7× of the spring limit.
Measured on the rope (projects 13, 21)
Substeps
(µs)
Result
667
50
reference
500
67
stable, 13.3 mm rms · 1.21×
444
75
stable, 8.3 mm drift · 1.49×
400
83
stable, 18.2 mm
334
100
diverges (NaN)
Rerun spread of the reference itself is 16.6 mm, so 500 substeps is “free”.
Why 667 Substeps: Explicit Stability
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
8

## Slide 9
•
A soft Dirichlet condition: prescribed motion through a compliant spring
•
Pulls as hard as it pushes
•
Never releases, never slips
•
Sparse: in single_push_rope only 2 of 30 hand points are within 40 mm
Tracked hand points are kinematic; springs tie them to nearby object particles
Hand points
Grounded-SAM2 hand masks + CoTracker → lifted to 3D → farthest-point sampled.
Attachment (frame 0, never changes)
Inside a frame: linear interpolation
What this boundary condition means
Code note: wp_control_v is never written, so the dashpot on control springs sees a control velocity of 0.
Good for fitting a video, wrong for robot grasping: a policy could “lift” the rope without ever squeezing it.
PhysTwin Control: Points Welded by Springs
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
9

## Slide 10
•
Read normal “force” on fixed finger faces
•
Latch when both fingers exceed a threshold (3×10⁴; 4,386 after our recalibration)
•
Release when both drop below a low threshold
Finger meshes and static scenery are one triangle mesh with a BVH, refit every substep
EEF pose
per frame
Interpolate
667 finger poses
One wp.Mesh
fingers + static
BVH refit
every substep
Rigid velocity of a finger point
xArm fingers: 88 triangles, 48 vertices. mesh_map[face] = 0 / 1 for the fingers, < 0 for static meshes.
Grasp is a force latch, not a weld
real2sim-eval: Gripper as a Moving Mesh
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
10

## Slide 11
Ground, self- and mesh contact all edit the velocity — no penalty springs
Split relative velocity along the normal
Restitution
Coulomb:
Reading the scale factor
Case
Meaning
stick: friction impulse can stop all sliding
slip: slide slowed by exactly normal impulse
grazing,
Clamps in the kernels
Same idea as the PushT impulse model — but applied per particle, per substep, with unit mass and no rotation.
One Contact Law: Restitution and Coulomb
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
11

## Slide 12
If the next step would cross while moving down, apply the law and split the step
Trigger
Time of impact, then two half-moves
Resting particle,
Gravity re-supplies of normal speed each substep → constant deceleration — textbook sliding friction.
spring_mass_warp.py : integrate_ground_collision
normal = wp.vec3(0.0, 0.0, 1.0) * reverse_factor
next_x_z = (x_z + v_z * dt) * reverse_factor
if next_x_z < 0.0 and v_z * reverse_factor < -1e-4:
v_normal = wp.dot(v0, normal) * normal
v_tao = v0 - v_normal
v_normal_new = -clamp_collide_elas * v_normal
a = wp.max(0.0, 1.0 - clamp_collide_fric
* (1.0 + clamp_collide_elas)
* v_normal_length / v_tao_length)
v1 = v_normal_new + a * v_tao
toi = -(x_z - ground_height) / v_z
else:
v1 = v0; toi = 0.0
x_new[tid] = x0 + v0 * toi + v1 * (dt - toi)
Ground Contact with Time of Impact
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
12

## Slide 13
Particles of different parts that approach closer than 5 mm exchange an impulse
Broad phase (once per frame)
wp.HashGrid, cell ; keep pairs with different masks and (≤ 500 per particle). Pairs already close at frame 0 are excluded.
Narrow phase: approaching pairs only
Parameters
Value
0.005 m (PhysTwin 0.02)
clamped to [0,1], [0,2]
averaging
Jacobi-style mean
What we found
In our project-13 bridge, update_collision_graph() was never called: the kernel ran 667×/frame and looped zero times. Upstream's driver does call it.
Self-Collision: Hash Grid, Then Impulses
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
13

## Slide 14
Every particle asks the BVH: “will I be inside a finger or the table next step?”
1. Predict and query (signed distance)
inside/outside by winding number; margin = 5 mm (finger), 1 mm (static).
2. If err < 0: law in the finger's frame
Fingers: . Static: ground values.
3. Project out, read force
spring_mass_warp.py : mesh_collision (condensed)
next_x = x0 + v0 * dt
query = wp.mesh_query_point_sign_winding_number(
mesh, next_x, max_dist=0.02,
accuracy=3.0, threshold=0.6)
p = wp.mesh_eval_position(mesh, query.face, ...)
err = wp.length(next_x - p) * query.sign - margin
if err < 0.0:
normal = wp.normalize(next_x - p) * query.sign
real_dynamic_velocity = dynamic_velocity[k] \
+ wp.cross(dynamic_omega[0], x0 - center)
v0 = v0 - real_dynamic_velocity
# ... restitution + Coulomb scale a ...
next_v = v_normal_new + a * v_tao \
+ real_dynamic_velocity
# finger: re-predict, query again, push out
next_x = next_x - normal * err
wp.atomic_add(collision_forces, face,
delta_v_normal / dt)
Mesh Contact: Query, Respond, Project
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
14

## Slide 15
Approach, close, lift: the rope rises only through the friction its own squeeze creates
Project 13: orange = finger meshes, blue = rope particles. Right: centre-of-mass rise (+62.9 mm), jaw opening (dashed), contact force (red).
Read the plot : the force spikes when the jaw closes, then settles at the value that holds the rope's weight — grip force × ≥ weight, or it slips.
Frictional Grasp: Lifted Without a Weld
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
15

## Slide 16
•
Once: hash grid, 667 interpolated finger poses
•
667 × (6 kernels + 1 refit) ≈ 4,000 launches
•
All kernels: one thread per spring or per particle
Six GPU kernels and one BVH refit — repeated 667 times for each 33 ms video frame
clear
springs
per spring
velocity
, drag
self
impulses
refit
finger BVH
mesh
query + law
ground
TOI,
Per frame (30 fps)
Colour key
blue spring–mass–damper · orange object contact · purple gripper geometry · green ground + integration
PhysTwin: same order, no mesh stages, plus set_control_points first.
One Substep, Kernel by Kernel
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
16

## Slide 17
Doubling the particles costs nothing — the simulator is launch-latency bound
Part (667 substeps)
ms/frame
Share
BVH refit (88 triangles)
29.5
28.0 %
eval_springs (34,090)
22.0
20.8 %
mesh_collision
14.6
13.8 %
object_collision (inert)
10.7
10.2 %
ground + integrate
9.8
9.3 %
update_vel
8.5
8.1 %
set_mesh_points
6.5
6.1 %
clear_forces
4.0
3.7 %
Fit over substep counts
2,002 vs 4,004 particles: 89.3 vs 88.8 ms.
Grouped : gripper contact path ≈ 46 %, springs ≈ 33 %, ground ≈ 9 %.
Refitting a 48-vertex mesh costs more than 34k springs — it is pure launch overhead.
Where the Time Goes (GPU, 4,004 Particles)
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
17

## Slide 18
Filtering particles with the gripper's box cut queries 656× — and the frame by 1.1 %
100,100 particles
× 667 substeps
AABB gate
66.77 M → 101,796
Frame time
257.1 → 254.2 ms
Cost per particle query (GPU)
Case
Time
BVH miss
0.007 ns
AABB test
0.018 ns
BVH hit
20 ns (2,933× a miss)
Why
The BVH's first box test already is a broad phase. Only 3.8 % of (particle, substep) pairs are real hits, and those are what cost time.
Profile before you optimise — the textbook fix attacked a cost that did not exist.
Lesson: A Broad Phase Did Not Help
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
18

## Slide 19
Remove launches, atomics and refits: 1.7× at 4k particles, 1.9× at 100k
Change
4,004
100,100
cache
+0.2 ms
−5.0 ms
per-particle spring gather, no atomics
+1.6 ms
−57.6 ms
fuse mesh contact + ground
−2.0 ms
−5.1 ms
static finger BVH in local frame
−11.8 ms
−11.6 ms
CUDA graph replay
−12.0 ms
−14.8 ms
total (with 500 substeps)
81.6 → 48.4
264.3 → 137.8
Two key tricks
Gather : each particle sums its own springs —
Local BVH : move the particle, not the mesh —
Result : 3,335 launches → 1 per frame, 2 kernels per substep, every rms inside the 22.9 mm upstream self-spread.
What Actually Made It Faster
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
19

## Slide 20
CPU: a spring solver with some contact — GPU: a contact solver with some springs
Role (4,004 particles)
CPU ms
GPU ms
CPU/GPU
spring–mass–damper
201.8 (60.5 %)
14.9 (15.4 %)
13.5×
gripper contact
103.1 (30.9 %)
66.7 (68.9 %)
1.5×
integration
16.6 (5.0 %)
7.3 (7.5 %)
2.3×
ground
12.2 (3.7 %)
7.9 (8.2 %)
1.5×
BVH refit alone
0.5
19.1
0.03×
Warp's CPU backend is a serial loop, so it measures work; the GPU measures latency.
Same change, two verdicts
Change
CPU
GPU
cache exp
−16.2 %
−0.6 %
local BVH
+5.9 %
−16.5 %
broad phase
≈ 0
≈ 0
GPU speed-up grows with size: 3.2× at 2k → 24× at 100k particles.
CPU vs GPU: The Ranking Inverts
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
20

## Slide 21
Project the physics onto a few coarse modes; treat contact as a constraint, not a force
18 — latent operator, not learned
6,006 DOF → 96. is the exact Schur complement (8e-14). A whole frame = one matvec with .
5.10× end-to-end at 2.32 mm (0.23 %) error.
19 — reduced contact constraint
Coulomb disk, solved by PGS; 4 implicit microsteps replace 667 substeps.
Scene
Speed-up
resting / sliding
3.78× / 2.55×
3 cm drop
2.89×
gripper approach
1.18×, 90 mm worst — failure
Reduced Models: Fewer Degrees of Freedom
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
21

## Slide 22
Identical inputs, different rope: atomic float sums reorder, and contact amplifies it
Project 15: two identical runs overlaid (red = second run). Left: quasi-static press, 0.38 mm. Right: lift and drop, 66 mm.
Why : in float32. A tiny difference decides whether a particle is inside the 5 mm margin — a contact appears or not.
8 replays of one nominal (RL, 17) : 27.2, 30.5, 30.3, 27.7, 27.9, 50.6, 30.2, 29.3 mm. The per-particle gather is bit-reproducible.
Contact Makes the Simulator Non-Repeatable
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
22

## Slide 23
Probes designed to excite one parameter also create the most noise
Project 15: nine textbook probes, each with contact %, repeat noise, SNR
Probe
Repeat noise
quasi-static press
1.2 mm
ring-down
3.7 mm
lateral drag
7.1 mm
lift-drop
44–99 mm
Noise tracks churn (contacts forming and breaking), not contact time.
Fisher design predicted 1.19×; actual fits: random wins 5/5 (p ≈ 0.004).
Contact Churn Limits What We Can Identify
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
23

## Slide 24
•
Simulation model : log-stiffness springs with axial dashpots, exponential drag, symplectic Euler at 50 µs
→
is set by the stiffest, shortest spring — 1.7× below the limit
•
Boundary condition : PhysTwin welds the hand with springs; real2sim-eval uses a moving mesh with friction
→
only the second can slip, drop, and be a fair test of a grasp
•
Contact model : for ground, self and mesh
→
Coulomb friction as a velocity scale factor, plus position projection
•
Cost : on a GPU, launches and refits dominate — not arithmetic, not the broad phase
•
Consequence : contact turns float round-off into mm-scale divergence — budget for it in RL and system ID
A rope twin is springs + one velocity-level contact law, run 667 times per frame
Summary
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
24

## Slide 25
•
Stability : derive for a chain of 3 masses — when is it tighter than one spring?
•
Friction : show that exactly when the needed friction impulse is
•
Grasp : with , what squeeze force holds a 50 g rope? Compare with the latch threshold
•
Weld vs friction : replay one trajectory in both models — where do they disagree?
•
Determinism : run the same frame 10 times with atomics, then with the gather kernel
•
Profiling : predict the CPU and GPU ranking of each kernel before you measure it
Exercises with the simulator
Try It Yourself
Sookmyung Women’s Univ. Autonomous Mechanical Systems Lab
25